## Slide 1
Water Temp (LED 1)
Blue = Water Temp Too Low
Green = Water Temp OK
Red Flashing + “High Water Temp” Message on Red Screen = Water Temp Too High
Yellow at same time as LED6 Red + “ECU Trip-Water Temp” Message on Red Screen = ECU Trip for high Water Temp
Fuel Pressure (LED 2)
Red Flashing + “Low Fuel Pressure” Message on Red Screen = Fuel Pressure Too Low
Green = Fuel Pressure OK
[No Alarms for High Fuel Pressure]
Yellow at same time as LED6 Red + “ECU-Trip-Fuel Press” Message on Red Screen = ECU Trip for Low Fuel Pressure
Battery Voltage (LED 3)
White = Battery Voltage Too Low
Green = Battery Voltage OK
[No Alarm for Voltage Too High and there is no ECU Trip for Battery Voltage High/Low]
Oil Temp (LED 4)
Blue = Oil Temp Too Low
Green = Oil Temp OK
Red Flashing + “High Oil Temp” Message on Red Screen = Oil Temp Too High
[No ECU Trip exists for Oil Temperature High/Low]
Oil Pressure (LED 5)
Red Flashing + “Low Oil Press” Message on Red Screen = Oil Pressure Too Low
Green = Oil Temp OK
Yellow Flashing + “High Oil Press” Message on Red Screen = Oil Pressure Too High
Yellow at same time as LED6 Red + “ECU Trip-Oil Press” Message on Red Screen = ECU Trip for Low Oil Pressure
ECU ‘Trip State’ (LED 6)
Green = OK (No ECU Trip Has Occurred)
Red = ECU has decided to Trip Engine Off
When Red LED is showing, there will be another LED showing Yellow. This Yellow LED will indicate exactly which ECU Trip has occurred
  ECU Trips Exist for 3 Conditions;
  High Water Temperature
  Low Oil Pressure
  Low Fuel Pressure
New Radical MXL2 Config
Rod Bender
Mobile +61 418 509 692

## Slide 2
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables
New ‘Status Variables’ set up on the Status Variable Tab

## Slide 3
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 4
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 5
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 6
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 7
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 8
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 9
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 10
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 11
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 12
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 13
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 14
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 15
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables
New Alarm – Don’t think this was in original Configuration…

## Slide 16
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables
2000 rpm and 16 psi alarm window

## Slide 17
Removed this condition so it still works without the engine running – 2nd July 2021
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 18
Removed this condition so it still works without the engine running – 2nd July 2021
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 19
Removed this condition so it still works without the engine running – 2nd July 2021
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 20
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 21
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 22
Removed this condition so it still works without the engine running – 2nd July 2021
Radical SR3 RSX Dash – AiM MXL2 NEW Configuration with Status Variables

## Slide 23
Radical SR3 RSX Dash – AiM MXL2 New Shift Light Configuration (per gear)
Changed to below LED pattern 26th July 2021… but still needs to be transmitted to Logger

## Slide 24
Radical SR3 RPE 1500cc Long Stroke Dyno Chart (wheel hp)

## Slide 25
Radical SR3 RSX Dash – AiM MXL2 ‘Parameters’ Configuration